# Computer Structure

### Exercise Number 6

### Single Cycle Architecture and Pipelining

Single-Cycle Architecture

- We wish to add the instruction lwR (load word R-format) to the single-cycle architecture. The instruction uses the R-type format and sums the registers in the rt and rs fields to obtain an address of a word which will be loaded into the register whose number is in the rd field.

Explain in words and draw on the attached diagram any necessary additions/modifications (if there are any) to the datapaths and control signals.

- We wish to add the instruction jr (jump register) to the single-cycle datapath. Add any necessary datapaths and control signals to the single-cycle data path and table below:

| Instruction | RegDst | ALUSrc | Memto-Reg | Reg-Write | Mem Read | Mem Write | Branch | ALUOps1 | ALUOp0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| R-format | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 |
| lw | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 |
| sw | X | 1 | X | 0 | 0 | 1 | 0 | 0 | 0 |
| Beq | X | 0 | X | 0 | 0 | 0 | 1 | 0 | 1 |
| Jr | x |  | x | 0 |  | 0 | 0 |  |  |

Pipelining

- What will be the forwarding paths in the following code:

add $2, $3, $4

add $4, $5, $6

add $5, $3, $4

- Identify all of the data dependencies in the following code. Which dependencies are data hazards that will be resolved via forwarding?

add $2, $5, $4

add $4, $2, $5

sw   $5, 100($2)

add $3, $2, $4

- Consider executing the following code on the pipelined datapath depicted in the figure from slide #18 from the Pipeline recitation (with the hazard detection unit and forwarding unit)

add 	$2, $3, $1

sub 	$4, $3, $5

add 	$5, $3, $5

add 	$7, $6, $1

add 	$8, $2, $6

At the end of the fifth cycle of execution, which registers are being read and which register will be written?